## Slide 1: Floating Point Representation
"Team Greybeard" - Alex, Austin, & Thomas
IEEE Standard 745-2008

## Slide 2: Representation
Single Precision
Made up of 3 parts
  Sign
  Exponent
  Mantissa (also called fraction)
Base 2 scientific notation
  Base number
  Raised to an exponent
Notes: Sign bit:
0 is positive
1 is negative
Exponent:
The exponent field contains 127 plus the true exponent for single-precision
Why?:
The exponent field needs to represent both positive and negative exponents. To do this, a bias is added to the actual exponent in order to get the stored exponent. For IEEE single-precision floats, this value is 127. Thus, an exponent of zero means that 127 is stored in the exponent field. A stored value of 200 indicates an exponent of (200-127), or 73.

## Slide 3: Single Precision
32 bits total
Sign bit
  0 for positive
  1 for negative
Exponent
  Biased against 127
  The base is always 2 (2x)
Notes: Sign bit:
0 is positive
1 is negative
Exponent:
The exponent field contains 127 plus the true exponent for single-precision
Why?:
The exponent field needs to represent both positive and negative exponents. To do this, a bias is added to the actual exponent in order to get the stored exponent. For IEEE single-precision floats, this value is 127. Thus, an exponent of zero means that 127 is stored in the exponent field. A stored value of 200 indicates an exponent of (200-127), or 73.

## Slide 4: Single Precision continued
32 bits total
Mantissa
  Implicit 1
Range of possible Representation
  ± 10-44.85 to 1038.53
Notes: In order to maximize the quantity of representable numbers, floating-point numbers are typically stored in normalized form. This basically puts the radix point after the first non-zero digit.
In base two the only possible non-zero digit is 1. Thus, we can just assume a leading digit of 1, and don't need to represent it explicitly. As a result, the mantissa has effectively 24 bits of resolution, by way of 23 fraction bits.

## Slide 5: Normalization
The decimal point has to be after the first digit for base 2 scientific notation
Normalization Example:
100.100 * 20
-> 1.00100 * 22 = NORMALIZED

## Slide 6: Special Values:
Zero: an exponent field of zero and a fraction field of zero
Infinity: The values +infinity and -infinity are denoted with an exponent of all 1s and a fraction of all 0s.
Not A Number: NaN's are represented by a bit pattern with an exponent of all 1s and a non-zero fraction. There are two categories of NaN: QNaN (Quiet NaN) and SNaN (Signalling NaN). A QNaN has the most significant fraction bit set. An SNaN has the most significant fraction bit clear.

## Slide 7: Exceptions
Invalid Operations
Division By Zero
Overflow
Underflow
Inexact Answers

## Slide 8
"For operations producing results in floating-point format, the default result of an operation that signals the invalid operation exception shall be a quiet NaN that should provide some diagnostic information."
7.2 Invalid operations
Notes: Negative numbers less than -(2-2-23) × 2127 (negative overflow)
Negative numbers greater than -2-149 (negative underflow)
Positive numbers less than 2-149 (positive underflow)
Positive numbers greater than (2-2-23) × 2127 (positive overflow)

## Slide 9: Operations Resulting in qNaN
a) any general-computational or signaling-computational operation on a signaling NaN
b) multiplication: multiplication(0, ∞) or multiplication(∞, 0)
c) fusedMultiplyAdd (computes (x × y ) + z as if with unbounded range and precision, rounding only once to the destination format): fusedMultiplyAdd(0, ∞, c) or fusedMultiplyAdd(∞, 0, c) unless c is a quiet NaN; if c is a quiet NaN then it is implementation defined whether the invalid operation exception is signaled
d) addition or subtraction or fusedMultiplyAdd: magnitude subtraction of infinities, such as: addition(+∞, −∞)
e) division: division(0, 0) or division(∞, ∞)
f) remainder: remainder(x, y), when y is zero or x is infinite and neither is NaN
g) squareRoot if the operand is less than zero
h) quantize when the result does not fit in the destination format or when one operand is finite and the other is infinite
i) conversion of a floating-point number to an integer format, when the source is NaN, infinity, or a value that would convert to an integer outside the range of the result format under the applicable rounding attribute
j) comparison by way of unordered-signaling predicates when the operands are unordered
k) logB(NaN), logB(∞), or logB(0) when logBFormat is an integer format

## Slide 10
Signal divideByZero only when:
For division, when the divisor is zero and the dividend is a finite non-zero number, the sign of the infinity is the exclusive OR of the operands’ signs
For logB(0) when logBFormat is a floating-point format, the sign of the infinity is minus (−∞).
7.3 Division by zero

## Slide 11: 7.4 Overflow
Signaled if the destination format’s largest finite number is exceeded in magnitude by what would have been the rounded floating-point result.
Under default exception handling for overflow, the overflow flag shall be raised and the inexact
exception shall be signaled.

## Slide 12: 7.5 Underflow
The underflow exception shall be signaled when a tiny non-zero result is detected. For binary formats, this
shall be either:
a) after rounding — when a non-zero result computed as though the exponent range were unbounded would lie strictly between ± bemin, or
b) before rounding — when a non-zero result computed as though both the exponent range and the precision were unbounded would lie strictly between ± bemin.
The implementer shall choose how tininess is detected, but shall detect tininess in the same way for all operations in radix two, including conversion operations under a binary rounding attribute.

## Slide 13: Underflow Flag
If the rounded result is inexact the underflow flag shall be raised and the inexact exception shall be signaled. If the rounded result is exact, no flag is raised and no inexact exception is signaled.
This is the only case in this standard of an exception signal receiving default handling that does not raise the corresponding flag.

## Slide 14: 7.6 Inexact
Inexact answers differ from what would
have been computed were both exponent range and precision unbounded.
In this case, the inexact exception shall be signaled and the rounded or overflowed result shall be delivered to the destination.